## Slide 1: Increasing Tape Efficiency
Original slides from HEPiX Fall 2008 Taipei
Nicola Bessone, German Cancio, Steven Murray, Giulia Taurelli

## Slide 2: Contents
Tape efficiency project
Problem areas
What has been done
What is under development
Roadmap and current status

## Slide 3: Tape Efficiency Project
All functionality dealing directly with storage on and management of tapes
  Volume database
  Migrations/recalls
  Tape drive scheduling
  Low-level tape positioning and read/write
Team is from IT/DM
Contributions from IT/FIO

## Slide 4: Problem Areas
Write more data per tape mount
Use a more efficient tape format
  The current tape format does not deal efficiently with small files
Improve read efficiency
  Require modifications from tape->disk
Work
done
Current
work
More
ideas

## Slide 5
What has
been done

## Slide 6: Read/write More Per Mount
Recall/migration policies
  Freight train approach
  Hold back requests based on the amount of data and elapsed time
Production managers rule
  Production managers plan relatively large workloads for CASTOR
  Access control lists give production managers a relatively larger percentage of resources
  User and group based priorities encourage users to work with their production managers

## Slide 7: Repack: Measurements
4 drives reading
7 drives writing
400MBytes/s
Writing the current ANSI AUL format is approximately twice as slow as reading. Repack uses the cache to support asymmetric read/write drive allocation

## Slide 8
What is under
development

## Slide 9: Writing Small Files is Slow
Chart: Average Filesize per VO
| alice | atlas | cms | compass | lhcb | na48 | other | user
filesize | 204.2468 | 155.209 | 2858.8003 | 893.2895 | 220.6293 | 74.3645 | 191.284 | 114.6366
Chart: Typical Drive Performance
| 0.25 | 0.5 | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 2500
Mbytes/s | 0.02 | 0.06 | 0.14 | 0.28 | 0.56 | 1.13 | 2.22 | 4.22 | 7.84 | 13.66 | 27.49 | 44.95 | 65.72 | 89.04 | 93
atlas | 72
lhcb | 72
Users were encouraged to store large files in Castor
Unfortunately Castor contains many small files

## Slide 10: Why Small Files are Slow
ANSI AUL format
3 tape marks per file
2 to 3 second per tape mark
9 seconds per data file independent of its size
hdr1
hdr2
uh1
tm
data file
tm
eof1
eof2
utl1
tm
Header
Trailer
Tape marks
1 data file

## Slide 11: New Tape Format
Multi-file block format within the ANSI AUL format
Header per block for “self description”
3 tape marks per n files
n will take into account:
  A configurable maximum number of files
  A configurable maximum size
  A configurable maximum amount of time to wait
data file 1
…
data file n
hdr1
hdr2
uh1
tm
tm
eof1
eof2
utl1
tm
Trailer
N data files
Header
Each 256 KB data file block written to tape includes a 1 KB header

## Slide 12: Block Header Format
# | Meta-data name | Explanation | Examples | Bytes for Data
1 | VERSION_NUMBER | The version of the block format | 09.13 | 5
2 | HEADER_SIZE | Header size in bytes | 01024 | 5
3 | CHECKSUM_ALGORITHM | Name of the checksum algorithm | Adler-32 | 10
4 | HEADER_CHECKSUM | Adler-32 checksum | 4146884724 | 10
5 | TAPE_MARK_COUNT | Sequential number addressing the migration-files on the tape | 00000000000000012345 | 20
6 | BLOCK_SIZE | Block size in bytes inclusive of header | 0000262144 | 10
7 | BLOCK_COUNT | Block offset from the beginning of the tape. Tape marks and labels are included in the count | 00000000000000012345 | 20
8 | BLOCK_TIME_STAMP | Time since the Epoch (00:00:00 UTC, January 1, 1970), measured in seconds | 1222332810 | 10
9 | STAGER_VERSION | The version of the stager software | 2.1.7.18 | 15
10 | STAGER_HOST | The DNS name of the stager host including the domain | c2cms2stager.cern.ch | 30
11 | DRIVE_NAME | Will be provided by a local configuration file | 0003592028 | 10
12 | DRIVE_SERIAL | Will be provided by a local configuration file | 00000000456000001642 | 20
13 | DRIVE_FIRMWARE | Will be provided by a local configuration file | D3I0_C90 | 10
14 | DRIVE_HOST | The DNS name of the host including the domain | tpsrv250.cern.ch | 30
15 | VOL_DENSITY | The storage capacity of the tape | 700.00GB | 10
16 | VOL_ID | Site specific numbering system (the sticker on a tape) | T02694 | 20
17 | VOL_SERIAL | Volume Serial Number | T02694 | 20
18 | DEVICE_GROUP_NAME | The device group name that linked the tape to the drive | 3592B1 | 10
19 | FILE_SIZE | The size of the data file in bytes | 00000001099511627776 | 20
20 | FILE_CHECKSUM | Adler-32 checksum | 1926860616 | 10
21 | FILE_NS_HOST | The DNS name of the host including the domain | castorns.cern.ch | 30
22 | FILE_NS_ID | The name server ID of the data file | 226994274 | 20
23 | FILE_PROGESSIVE_CHECKSUM | Adler-32. Progressive checksum of all the blocks written to tape so far for the current data file | 1234567890 | 10
24 | FILE_BLOCK_COUNT | Block offset from the beginning of the data file | 00000000000000012345 | 20
 |  | Header size before file_name : |  | 375
25 | FILE_NAME | Last “x” bytes of the filename from the name server. This field acts as a padding to the nearest KiB. |  | 649
 |  | Header size : |  | 1024
VERSION_NUMBER
HEADER_SIZE
CHECKSUM_ALGORITHM
HEADER_CHECKSUM
TAPE_MARK_COUNT
BLOCK_SIZE
BLOCK_COUNT
BLOCK_TIME_STAMP
STAGER_VERSION
STAGER_HOST
DRIVE_NAME
DRIVE_SERIAL
DRIVE_FIRMWARE
DRIVE_HOST
VOL_DENSITY
VOL_ID
VOL_SERIAL
DEVICE_GROUP_NAME
FILE_SIZE
FILE_CHECKSUM
FILE_NS_HOST
FILE_NS_ID
FILE_PROGESSIVE_CHECKSUM
FILE_BLOCK_COUNT
FILE_NAME

## Slide 13: Predicted Tape Format Performance
Chart: Days Taken Using 20 Drives
| 0 | 83.470370370370318 | 123.48333333333331 | 144.54467592592539 | 157.41828703703757 | 171.56203703703767 | 183.54583333333341 | 192.53009259259258 | 200.57430555555558 | 209.70208333333341 | 216.92106481481483 | 222.58287037037044 | 227.57013888888889 | 232.55023148148203 | 236.81273148148193 | 241.75694444444443 | 245.2731481481475 | 248.0645833333333 | 251.07129629629625 | 253.85555555555553 | 256.71874999999892 | 302.43657407407233
il,max80 | 0 | 0.27599 | 0.40829 | 0.47793 | 0.5205 | 0.56727 | 0.60689 | 0.6366 | 0.66319 | 0.69338 | 0.71724 | 0.73597 | 0.75246 | 0.76892 | 0.78302 | 0.79936 | 0.81099 | 0.82022 | 0.83016 | 0.83937 | 0.84884 | 1
aul,max25 | 0 | 0.27599 | 0.40829 | 0.47793 | 0.5205 | 0.56727 | 0.60689 | 0.6366 | 0.66319 | 0.69338 | 0.71724 | 0.73597 | 0.75246 | 0.76892 | 0.78302 | 0.79936 | 0.81099 | 0.82022 | 0.83016 | 0.83937 | 0.84884 | 1
New tape format
AUL tape format
Less than 1 year with the new tape format
Greater than 4 years with the AUL tape format
Hardware manufactures increasing tape density impose a 2 year cycle
The future of repack may be to run continuously to verify checksums and ensure data integrity

## Slide 14: Architecture Needs to Change
The new tape format is only half of the story
An aggregator needs to be inserted into the disk ↔ tape data streams
Anything old that is replaced is an opportunity for code re-use and increased maintainability via the Castor framework

## Slide 15: Current Architecture
Drive
Scheduler
Tape
Server
Disk
Server
Disk
Server
Disk
Server
1
2
1. Stager requests a drive
2. Drive is allocated
3. Data is transferred to/from disk/tape
based on file list given by stager
3
3
Legend
Data
Control messages
Host
Stager
Stager
Stager
1 data file
=
1 tape file

## Slide 16: New Architecture
Stager
Stager
Drive
Scheduler
Tape Server
Disk
Server
Disk
Server
Disk
Server
Stager
Legend
Data to be stored
Control messages
Host
Server process(es)
Tape Gateway
Tape Aggregator
n data files
=
1 tape file
The tape gateway will replace RTCPClientD
The tape gateway will be stateless
The tape aggregator will wrap RTCPD

## Slide 17: Roadmap
Date | Actions
Beginning Q4 2008 | Put repack into full production will at least 20 drives. Expecting 700 MB/s. Conclude new tape format architecture.
End Q1 2009 | Release first functional prototype of new tape format.
End Q2 2009 | Write new tape format with repack only. Read new tape format everywhere.
End Q3 2009 | Read and write everywhere
Beginning Q1 2010 | Replace RTCPD with tape aggregator
Current status (Feb 2009):
New tape format specified
Classes for reading/writing new format coded
Communication between rtcpclientd/rtcpd/VDQM reverse engineered and understood
Tape aggregator and gateway prototypes underway; first goal to fully support non-aggregated AUL read/writes; aggregations to come later