## Slide 1: Castor Database Operations @ CNAF
Castor F2F Meeting
Barbara Martelli

## Slide 2: Software versions
6 Oracle servers:
  RedHat Enterprise 5.1.2-21
  EMC PowerPath 5.1 (path failover/load balancing, device persistency)
Storage: 2 TB of raw disk space on EMC Clariion CX3-80
  ASM with 2 disk groups (DATA, RECOVERY) shared among DLF, Stager, Nameserver
  Local storage for SRM and Repack instances
Oracle 10.2.0.4 plus October ’08 CPU patch
Castor 2.1.7-17
SRM 1.3-28

## Slide 3: CASTOR Oracle DBs Setup
stager1
stager2
dlf1
dlf2
namesrv2
namesrv1
ASM
Data-DG
Recovery-DG
Oracle RAC 10.2.0.4
Oct08 CPU patch
srmv2
RHEL 5.2
PowerPath 5.1
Oracle 10.2.0.4
Single instance
repack
Oracle 10.2.0.4
Single instance
For each service, TAF policy is basic, one node active, one available, the remaining two not used

## Slide 4: Present Storage Usage
DB Service | Data /Flash Recovery Area | Redo Log activity per day | Active sessions
Stager | 9 GB/301 GB | 48 GB | 170
Nameserver | 3 GB/8 GB | 512 MB | 45
DLF | 98/113 GB | 6 GB | 20
SRM | 4 GB/9 GB | 512 MB | 130
Repack | 2GB/15GB | / | /
RMAN backups
  Retention policy: recovery windows range from 2 to 7 days
  Incremental backups (L0 weekly, L1 daily)
Used space calculated on space actually used (not only allocated) by castor instances plus Oracle SYSTEM tablespace

## Slide 5: Issues and evolution
Presently we are experiencing DB deadlocks on SRM instance, this should be solved with the next upgrade.
  SRM upgrade to 2.1.7-10 is ongoing
Still need to run few SQL manually for Castor maintenance (restart of migrator or rtcpClientD) but the situation has improved very much
Where can T1s get the oracle clients for SLC?
  oracle-instantclient-basic-10.2.0.3-3.slc4.x86_64
January ’09 CPU path by the end of March
SRM and Repack schemas will be moved on a new Oracle RAC by the end of March

## Slide 6: Monitoring/Alarms
Grid Control is used to monitor databases and their related hardware
  Use a single tool to ease management
  Use standard and customized metrics (ORA-00600, DB deadlocks, low disk space)
Alarms sent via email -> planning to set up SMS alarms for some critical events
  DB service down
  Storage failure (quite unlikely thank to redundancy)
Dash boards with group of related applications